## Slide 1: Dot Basics
Howard Parkin
Dot Manager Profrac Services

## Slide 2: Agenda
Intrastate Vs. Interstate
ELD requirements
State Vs. Federal Dot
Setting up new company DOT

## Slide 3: Who am I?
I am Howard Parkin, 20 year veteran of Wyoming Highway Patrol. I have 2 years driving experience,15 years of CMV enforcement experience and 8 years company compliance experience

## Slide 4: Intra state Vs. Interstate
What is the difference?

## Slide 5: Intra State
Never leaving one state jurisdiction
Crossing state lines with 150 air miles
Weight exceeds 26,001 lbs GVWR
CDL required (title 49 part 383)
Medical card required (title 49 part 391)
Driver logs not required if returning to start location.( Shorthaul exemption(title 49 part 395.1(e)(1))
Annual DOT/State inspection required

## Slide 6: Interstate
Crossing state lines
Weight over 10,001 lbs to 26,000 lbs (possible no CDL required)
Weight over 26,001 lbs CDL required
Medical card required
Driver logs required
Annual DOT inspection on vehicles

## Slide 7: ELD Requirements
What is required?

## Slide 8: ELD-Electronic logging Device
Driver responsible for accuracy
Employer required to verify accuracy
Must be connected to the vehicle
Drive time cannot be changed by driver or employer
Driver must have access to records
Special driving options can be set by employer
Must be on FMCSA national ELD provider registry
Most offer a Daily Vehicle Inspection Report option

## Slide 9: State Vs. Federal DOT
What is the difference?

## Slide 10: State Dot vs. Federal Dot
Most states codify Federal DOT regulations
Most states allow Highway Patrol officers and local specially trained jurisdictions to enforce DOT regulations
Legal Length/ Weights vary by state statutes
States allow HOS regulation variance for intra-state operators

## Slide 11: Setting up DOT #
What is the process?

## Slide 12: Setting up dot #
File application with FMCSA, upto 2 weeks to process
Set-up driver qualification files
Set-up vehicle maintenance files
Select ELD provider
Set-up Drug testing program

## Slide 13: THANK YOU
Howard Parkin – DOT Manager Profrac Services
Howard.Parkin@profrac.com
FMCSA.dot.gov